## Slide 1: Chapter-3
Introduction to Verilog HDL
FPGA Design flow using Verilog HDL

## Slide 2: Hardware Description Languages
In the beginning HDLs were developed as a ‘standard way’ of drawing circuit schematics.
Modeled the interface of circuits, described how they were connected
Allowed connections between these modules
Supported some common logic functions
  AND OR NOT XOR
  Multiplexers
The functionality of hardware
  concurrency
  timing controls
The implementation of hardware
  structure
  net-list

## Slide 3: History of HDLs
ISP (circa 1977) - research project at CMU
  Simulation, but no synthesis
Abel (circa 1983) - developed by Data-I/O
  Targeted to programmable logic devices
  Not good for much more than state machines
Verilog (circa 1985) - developed by Gateway (now Cadence)
  Similar to Pascal and C
  Delays is only interaction with simulator
  Fairly efficient and easy to write
  IEEE standard
VHDL (circa 1987) - DoD sponsored standard
  Similar to Ada (emphasis on re-use and maintainability)
  Simulation semantics visible
  Very general but verbose
  IEEE standard

## Slide 4: Convenient Way of Drawing Schematics

## Slide 5: Convenient Way of Drawing Schematics
It is standard
  Everybody will interpret the schematic the same way
It is not proprietary
  HDLs are not tool specific
It is machine readable
  It is easier for computers to understand the circuit
Only later on additional benefits were discovered
  Simulation and Synthesis

## Slide 6: Two Hardware Description Languages
Verilog
  developed in 1984 by Gateway Design Automation
  became an IEEE standard (1364) in 1995
  More popular in US
VHDL (VHSIC Hardware Description Language)
  Developed in 1981 by the Department of Defense
  Became an IEEE standard (1076) in 1987
  More popular in Europe
In this course we will use Verilog

## Slide 7: Introduction and Basic Concept
What is Verilog?
  Hardware Description Language(HDL)
Why use Verilog?
  Because 60% of US companies use it.

## Slide 8: Verilog
What’s an HDL?
  Textual description of a circuit.
  Human and machine readable.
  Hierarchical.
Verilog is NOT A PROGRAM
  Describe what the circuit IS.
  Not what is DOES.

## Slide 9: Why Verilog?
Why use an HDL?
  Describe complex designs (millions of gates)
  Input to synthesis tools (synthesizable subset)
  Design exploration with simulation
Why not use a general purpose language
  Support for structure and instantiation
  Support for describing bit-level behavior
  Support for timing
  Support for concurrency
Verilog vs. VHDL
  Verilog is relatively simple and close to C
  VHDL is complex and close to Ada
  Verilog has 60% of the world digital design market (larger share in US)

## Slide 10
Why Verilog?

## Slide 11: Modeling Structure: Modules
The module is the basic building block in Verilog
  Modules can be interconnected to describe the structure of your digital system
  Modules start with keyword module and end with keyword endmodule
  Modules have ports for interconnection with other modules
Module AND <port list>
•
•
•
endmodule
Module CPU <port list>
•
•
•
endmodule

## Slide 12: Verilog HDL and Verilog-XL
Verilog HDL
  Hardware design language that allows you to design circuit.
Verilog-XL
  High speed, event-driven simulator that reads Verilog HDL and simulates the behavior of hardware.

## Slide 13: Modern Project Methodology
Synthesis
Place and Route
clb 1
clb 2
Always
inst1
inst2
inst3
mapping

## Slide 14: Levels of design description
Algorithmic level
Register Transfer Level
Logic (gate) level
Circuit (transistor) level
Physical (layout) level
Level of description
most suitable for synthesis

## Slide 15: Different Levels of Abstraction
Algorithmic
  the function of the system
RTL
  the data flow
  the control signals
  the storage element and clock
Gate
  gate-level net-list
Switch
  transistor-level net-list

## Slide 16: Register Transfer Level (RTL) Design Description
Combinational
Logic
Combinational
Logic
Registers
…

## Slide 17: Verilog for Digital System Design
Structural description
  net-list using primitive gates and switches
  continuous assignment using Verilog operators
RTL
  functional description
  timing controls and concurrency specification
  procedural blocks (always and initial)
  registers and latches
C + timing controls + concurrency

## Slide 18: Behavioral vs Structural
Behavioral description describes functionality of design. It is independent of implementation.
  There is a one-to-many mapping between a behavioral module and a structural module.
Structural description defines and decides on an implementation of a module.
  Here we map the design to actual cells/gates.

## Slide 19: Behavioral vs. Structural (2)
Rule of thumb:
  Behavioral doesn’t have sub-components
  Structural has sub-components:
    Instantiated Modules
    Instantiated Gates
    Instantiated Primitives
Most modules are mixed
  Obviously this is the most flexible

## Slide 20: Behavioral vs. Structural

## Slide 21
Consider a I-bit equality comparator with two inputs, iO and il, and an output, eq. The eq signal is asserted when iO and il are equal. Assume that we want to use basic logic gates, which include not, and, or, and xor cells, to implement the circuit. One way to describe the circuit is to use a sum-of-products format. The logic expression is
Gate-level implementation of a I-bit comparator
Graphical representation of a comparator program.

## Slide 29: Hierarchical structure and Modules
Represent the hierarchy of a design
  modules
    the basic building blocks
  ports
    the I/O pins in hardware
    input, output or inout

## Slide 30: Event Driven Simulation
Verilog is really a language for modeling event-driven systems
  Event : change in state
  Simulation starts at t = 0
  Processing events generates new events
  When all events at time t have been processed simulation time advances to t+1
  Simulation stops when there are no more events in the queue
•••
0
t t+1
•••
Event
queue
Events

## Slide 31: Modeling Structure: Modules
The module is the basic building block in Verilog
  Modules can be interconnected to describe the structure of your digital system
  Modules start with keyword module and end with keyword endmodule
  Modules have ports for interconnection with other modules
Module AND <port list>
•
•
•
endmodule
Module CPU <port list>
•
•
•
endmodule

## Slide 32: Modeling Structure: Ports
Module Ports
  Similar to pins on a chip
  Provide a way to communicate with outside world
  Ports can be input, output or inout
i0
i1
o
Module AND (i0, i1, o);
input i0, i1;
output o;
endmodule

## Slide 33: Modeling Structure: Instances
Module instances
  Verilog models consist of a hierarchy of module instances
  In C++ speak: modules are classes and instances are objects
AND3
i0
i1
i2
o
Module AND3 (i0, i1, i2, o);
input i0, i1, i2;
output 0;
wire temp;
AND a0 (.i0(i0), .i1(i1), .o(temp));
AND a1 (.i0(i2), .i1(temp), .o(0));
endmodule

## Slide 34: Logic Values
0: zero, logic low, false, ground
1: one, logic high, power
X: unknown
Z: high impedance, unconnected, tri-state

## Slide 35: Variable Declaration
Declaring a net
  wire [<range>] <net_name> [<net_name>*];
  Range is specified as [MSb:LSb]. Default is one bit wide
Declaring a register
  reg [<range>] <reg_name> [<reg_name>*];
Declaring memory
  reg [<range>] <memory_name> [<start_addr> : <end_addr>];
Examples
  reg r; // 1-bit reg variable
  wire w1, w2; // 2 1-bit wire variable
  reg [7:0] vreg; // 8-bit register
  reg [7:0] memory [0:1023]; a 1 KB memory

## Slide 36: Modules
The principal design entity
Module Name &
Port List
Definitions
Ports, Wire, Reg,
Parameter
Module
Instatiations
Module Statements &
Constructs

## Slide 37: Modules are circuit components
Module has ports
  External connections
  A,B,C,X,Y in example
Port types
  input
  output
  inout (tristate)
Use assign statements for Boolean expressions
  and  &
  or  |
  not  ~
// previous example as a
// Boolean expression
module simple2 (X,Y,A,B,C);
input A,B,C;
output X,Y;
assign X = (A&B)|~C;
assign Y = ~C;
endmodule

## Slide 38
Modeling Digital Systems
Verilog HDL is for writing models of a system
Reasons for modeling
  requirements specification
  documentation
  testing using simulation
  formal verification
  synthesis
Goal
  most reliable design process, with minimum cost and time
  avoid design errors!

## Slide 39: There are Two Main Styles of HDL (Verilog)
Structural
  Describe how modules are interconnected
  Each module contains other modules (instances)
  … and interconnections between these modules
  Describes a hierarchy
Behavioral
  The module body contains functional description of the circuit
  Contains logical and mathematical operators
Practical circuits would use a combination of both

## Slide 40
Domains and Levels of Modeling
high level of abstraction
Functional
Structural
Geometric
low level of abstraction

## Slide 41
Domains and Levels of Modeling
Functional
Structural
Geometric
Algorithm (behavioral)
Register-Transfer Language
Boolean Equation
Differential Equation

## Slide 42
Domains and Levels of Modeling
Functional
Structural
Geometric
Processor-Memory Switch
Register-Transfer
Gate
Transistor

## Slide 43
Domains and Levels of Modeling
Functional
Structural
Geometric
Polygons
Sticks
Standard Cells
Floor Plan

## Slide 44
Structural vs Behavioral Models
Structural model
  Just specifies primitive gates and wires
  i.e., the structure of a logical netlist
  You basically know how to do this now.
Behavioral model
  More like a procedure in a programming language
  Still specify a module in Verilog with inputs and outputs...
  ...but inside the module you write code to tell what you want to have happen, NOT what gates to connect to make it happen
  i.e., you specify the behavior you want, not the structure to do it
Why use behavioral models
  For test bench modules to test structural designs
  For high-level specs to drive logic synthesis tools

## Slide 45: Structural Modeling
Structural Verilog describes connections of modules (netlist)
and a0(.i0(a), .i1(b), .o(out));

## Slide 46: Structural Verilog
module xor_gate (out,a,b); input a,b; output out; wire abar, bbar, t1, t2; not inva (abar,a); not invb (bbar,b); and and1 (t1,abar,b); and and2 (t2,bbar,a); or or1 (out,t1,t2);
endmodule
8 basic gates (keywords):
and, or, nand, nor
buf, not, xor, xnor

## Slide 48: Example
4-bit adder
    module add4 (s,c3,ci,a,b)
    input [3:0] a,b ; // port declarations
    input ci ;
    output [3:0] s : // vector
    output c3 ;
    wire [2:0] co ;
      add a0 (co[0], s[0], a[0], b[0], ci) ;
      add a1 (co[1], s[1], a[1], b[1], co[0]) ;
      add a2 (co[2], s[2], a[2], b[2], co[1]) ;
      add a3 (c3, s[3], a[3], b[3], co[2]) ;
  endmodule
a0
a1
a2
a3
c3
ci
Simpler than VHDL
Only Syntactical
Difference

## Slide 49: Behavioral Verilog
Describe circuit behavior
  Not implementation
A
B
Cin
Cout
Sum
Adder
module full_addr (Sum,Cout,A,B,Cin); input A, B, Cin; output Sum, Cout; assign {Cout, Sum} = A + B + Cin; endmodule
{Cout, Sum} is a concatenation

## Slide 50: Behavioral 4-bit adder
module add4 (SUM, OVER, A, B);
input [3:0] A;
input [3:0] B;
output [3:0] SUM;
output OVER;
assign {OVER, SUM[3:0]} = A[3:0] + B[3:0];
endmodule
“[3:0] A” is a 4-wire bus labeled “A”
Bit 3 is the MSB
Bit 0 is the LSB
Can also write “[0:3] A”
Bit 0 is the MSB
Bit 3 is the LSB
Buses are implicitly connected—
If you write BUS[3:2], BUS[1:0],
they become part of BUS[3:0]

## Slide 51: Major Data Type Class
Nets
Registers
Parameters

## Slide 52: Nets
Net data type represent physical connections between structural entities.
A net must be driven by a driver, such as a gate or a continuous assignment.
Verilog automatically propagates new values onto a net when the drivers change value.

## Slide 53: Data types
Net
  physical wire between devices
  the default data type
  used in structural modeling and continuous assignment
  types of nets
    wire, tri : default
    wor, trior : wire-ORed
    wand, triand : wire-ANDed
    trireg : with capacitive storage
    tri1 : pull high
    tri0 ; pull low
    supply1 ; power
    supply0 ; ground

## Slide 54: Reg and Parameters
Reg
  variables used in RTL description
  a wire, a storage device or a temporary variable
  reg : unsigned integer variables of varying bit width
  integer : 32-bit signed integer
  real : signed floating-point
  time : 64-bit unsigned integer
Parameters
  run-time constants

## Slide 55: Verilog Simulator
Circuit Description
Testfixture
Verilog Simulator
Simulation Result

## Slide 56: Sample Design
module fadder ( sum, cout, a, b , ci );
// port declaration
output sum, cout;
input a, b, ci;
reg sum, cout;
// behavior description
always @( a or b or ci )
begin
sum = a ^ b ^ ci;
cout = ( a&b ) | ( b&ci ) | ( ci&a);
end
endmodule
1-bit full adder
a
b
ci
sum
cout
Simpler than VHDL
Only Syntactical Difference

## Slide 57: Basic Instructions

## Slide 58: Lexical Conventions in Verilog
Type of lexical tokens :
Operators ( )
White space
Comment
Number ( )
String
Identifier
Keyword ( )

## Slide 59: Special Language Tokens
$<identifier>: System tasks and functions
  $time
  $stop
  $finish
  $monitor
  $ps_waves
  $gr_waves
  $gr_regs
#<delay specification>
  used in
    gate instances and procedural statements
    unnecessary in RTL specification

## Slide 60: Modeling Structures
Net-list
  structural description for the top level
Continuous assignments (combination circuits)
  data flow specification for simple combinational
  Verilog operators
Procedural blocks (RTL)
  always and initial blocks
    allow timing control and concurrency
  C-like procedure statements
primitives (=truth table, state transition table)
function and task (»function and subroutine)

## Slide 61: A full-adder
module add (co, s, a, b, c)
    input a, b ,c ;
    output co, s ;
      xor (n1, a, b) ;
      xor (s, n1, c) ;
      nand (n2, a, b) ;
      nand (n3,n1, c) ;
      nand (co, n3,n2) ;
  endmodule

## Slide 62: Verilog Primitives
Basic logic gates only
  and
  or
  not
  buf
  xor
  nand
  nor
  xnor
  bufif1, bufif0
  notif1, notif0

## Slide 63: Primitive Pins Are Expandable
One output and variable number of inputs
not and buf
  variable number of outputs but only one input
nand (y, in1, in2) ;
nand (y, in1, in2, in3) ;
nand (y, in1, in2, in3, in4) ;

## Slide 64: Continuous Assignments
Describe combinational logic
Operands + operators
Drive values to a net
  assign out = a&b ; // and gate
  assign eq = (a==b) ; // comparator
  wire #10 inv = ~in ; // inverter with delay
  wire [7:0] c = a+b ; // 8-bit adder
Avoid logic loops
  assign a = b + a ;
  asynchronous design

## Slide 65: Logical and Conditional Operators
Logical, bit-wise and unary operators
  a = 1011; b = 0010
  logical bit-wise unary
  a || b = 1 a | b = 1011 |a = 1
  a && b = 1 a &b = 0010 &a = 0
Conditional operator
  assign z = ({s1,s0} == 2'b00) ? IA :
  ({s1,s0} == 2'b01) ? IB :
  ({s1,s0} == 2'b10) ? IC :
  ({s1,s0} == 2'b11) ? ID :
  1'bx ;
  assign s = (op == ADD) ? a+b : a-b ;

## Slide 66: Continuous assignment
Assignment is continuously evaluated
  Corresponds to a logic gate
  Assignments execute in parallel
assign A = X | (Y & ~Z);
assign B[3:0] = 4'b01XX;
assign C[15:0] = 16'h00ff;
assign #3 {Cout, Sum[3:0]} = A[3:0] + B[3:0] + Cin;
gate delay (used by simulator)
Boolean operators (~ for bit-wise negation)
bits can assume four values (0, 1, X, Z)
variables can be n-bits wide (MSB:LSB)

## Slide 67: Invalid sequential assigns
assign A = X | (Y & ~Z);
assign B = W | A;
assign A = Y & Z;
“Reusing” a variable on the left
side of several assign statements is not allowed
assign A = X | (Y & ~Z);
assign B = W | A;
assign X = B & Z;
Cyclic dependencies also are bad
A depends on X
which depends on B
which depends on A

## Slide 68: Example: 4-bit comparator
module Compare1 (Equal, Alarger, Blarger, A, B); input A, B; output Equal, Alarger, Blarger; assign Equal = (A & B) | (~A & ~B); assign Alarger = (A & ~B); assign Blarger = (~A & B); endmodule
Starting with 1-bit comparator
  Top-down design and bottom-up design are both okay
  Module ordering doesn’t matter because modules execute in parallel

## Slide 69: 4-bit comparator
// Make a 4-bit comparator from 4 1-bit comparators module Compare4(Equal, Alarger, Blarger, A4, B4); input [3:0] A4, B4; output Equal, Alarger, Blarger; wire e0, e1, e2, e3, Al0, Al1, Al2, Al3, B10, Bl1, Bl2, Bl3; Compare1 cp0(e0, Al0, Bl0, A4[0], B4[0]); Compare1 cp1(e1, Al1, Bl1, A4[1], B4[1]); Compare1 cp2(e2, Al2, Bl2, A4[2], B4[2]); Compare1 cp3(e3, Al3, Bl3, A4[3], B4[3]); assign Equal = (e0 & e1 & e2 & e3); assign Alarger = (Al3 | (Al2 & e3) |
(Al1 & e3 & e2) |
(Al0 & e3 & e2 & e1)); assign Blarger = (~Alarger & ~Equal); endmodule

## Slide 70: Functions
Use functions for complex combinational logic
module and_gate (out, in1, in2); input in1, in2; output out;
assign out = myfunction(in1, in2);
function myfunction;
input in1, in2;
begin
myfunction = in1 & in2;
end
endfunction
endmodule
Benefit:
Functions force a result
 Compiler will fail if function
does not generate a result

## Slide 71: Always code blocks
reg A, B, C;
always @ (W or X or Y or Z)
begin
A = X | (Y & ~Z);
B = W | A;
A = Y & Z;
if (A & B) begin
B = Z;
C = W | Y;
end
end
Sensitivity list:
block is executed
each time one of
them changes value
Variables that appear on the left hand side in an always block must be declared as “reg”s
Statements in an always block are executed in sequence
BAD: All variables must be assigned on every control path!!!

## Slide 72: Assignments
Blocking assignments (Q = A)
  Variable is assigned immediately
    New value is used by subsequent statements
Non-blocking assignments (Q <= A)
  Variable is assigned after all scheduled statements are executed
    Value to be assigned is computed but saved for later parallel assignment
  Usual use: Register assignment
    Registers simultaneously take new values after the clock edge

## Slide 73: Blocking vs. non-blocking
Example: Swap
always @(posedge CLK) begin temp = B; B = A; A = temp; end
always @(posedge CLK) begin A <= B; B <= A; end

## Slide 74: Operators
{}
Concatenations
?:
Conditional Operators
>>, <<
Shift Operators
&, ~&, |, ~|, ^, ~^
Unary Reduction
~, &, |, ^, ~^
Bit-Wise Operators
!, &&, ||
Logical Operators
==, !=, ===, !==
Equality Operators
<, <=, >, >=
Relational Operators
+, -, *, /, %
Arithmetic Operators

## Slide 75: Operator Precedence
[ ] bit-select or part-select
( ) parentheses
!, ~ logical and bit-wise negation
&, |, ~&, ~|, ^, ~^, ^~ reduction operators
+, - unary arithmetic
{ } concatenation
*, /, % arithmetic
+, - arithmetic
<<, >> shift
>, >=, <, <=
relational
==, != logical equality
& bit-wise AND
^, ^~, ~^
bit-wise XOR and XNOR
| bit-wise OR
&& logical AND
|| logical OR
? : conditional

## Slide 76: Operators
{ } concatenation
+ - * /
arithmetic
% modulus
> >= < <=
relational
! logical NOT
&& logical AND
|| logical OR
== logical equality
!= logical inequality
? : conditional
~ bit-wise NOT
& bit-wise AND
| bit-wise OR
^ bit-wise XOR
^~ ~^ bit-wise XNOR
& reduction AND
| reduction OR
~& reduction NAND
~| reduction NOR
^ reduction XOR
~^ ^~ reduction XNOR
<< shift left
>> shift right

## Slide 77: Simple Behavioral Model: the always block
always block
  Always waiting for a change to a trigger signal
  Then executes the body
module and_gate (out, in1, in2); input in1, in2; output out; reg out; always @(in1 or in2) begin
out = in1 & in2;
end
endmodule
Not a real register!!
A Verilog register
Needed because of
assignment in always block
Specifies when block is executed I.e., triggered by which signals

## Slide 78: always Block
Procedure that describes the function of a circuit
  Can contain many statements including if, for, while, case
  Statements in the always block are executed sequentially
    (Continuous assignments <= are executed in parallel)
  Entire block is executed at once
  Final result describes the function of the circuit for current set of inputs
    intermediate assignments don’t matter, only the final result
begin/end used to group statements

## Slide 79: Verilog while/repeat/forever
while (expression) statement
  Execute statement while expression is true
repeat (expression) statement
  Execute statement a fixed number of times
forever statement
  Execute statement forever

## Slide 80: Numbers
Format : <size>’<base><value>
Example : 8’d16
8’h10
8’b00010000
8’o20

## Slide 81: Keywords
Note : All keywords are defined in lower case
Examples :
module, endmodule
input, output, inout
reg, integer, real, time
not, and, nand, or, nor, xor
parameter
begin, end
fork, join
specify, endspecify

## Slide 82: Value Set in Verilog
‘0’
‘1’
‘X’
‘Z’
0
4-value logic system in Verilog :

## Slide 83: Registers & Parameters
Registers represent abstract storage elements.
A register holds its value until a new value is assigned to it.
Registers are used extensively in behavior modeling and in applying stimuli.
Parameters are not variables, they are constants.

## Slide 84: Assignments
Assignment : drive values into nets and registers.
Continuous Assignments – Any changes in the RHS of continuous assignment are evaluated and the LHS is update.
Example : (1) assign out = ~in;
(2) assign reg_out; = reg_in << shift

## Slide 85: Assignments ( cont. )
Blocking procedural assignment.
rega = regb + regc;
Non-blocking procedural assignment.
rega <= regb * regc;

## Slide 86: Blocking vs. Non-Blocking (1)
always @ (a) begin
b = a;
c = b;
end
always @ (posedge Clock) begin
b <= a;
c <= b;
end
C = B = A
A-----B-------C
B = Old A
C = Old B
Verilog Fragment
Result
B
D
Q
C
D
Q
A
Clock

## Slide 87: Blocking vs. Non-Blocking (2)
Use Non-Blocking for FlipFlop Inference
  posedge/negedge require Non-Blocking
  Else simulation and synthesis wont match

## Slide 88: Blocking vs. Non-Blocking (3)
If you use blocking for FlipFlops:
YOU WILL NOT GET WHAT YOU WANT!
always @ (posedge Clock) begin
b = a; // b will go away
c = b; // c will be a FlipFlop
end
// b isn’t needed at all
always @ (posedge Clock) begin
c = b; // c will be a FlipFlop
b = a; // b will be a FlipFlop
end

## Slide 90: Defining a module
A module is the main building block in Verilog
We first need to declare:
  Name of the module
  Types of its connections (input, output)
  Names of its connections

## Slide 91: Defining a module
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
endmodule

## Slide 92: A question of style
module test ( a, b, y );
input a;
input b;
output y;
endmodule
module test ( input a,
input b, output y );
endmodule
The following two codes are identical

## Slide 93: What if we have busses?
input [31:0] a; // a[31], a[30] .. a[0]
output [15:8] b1; // b1[15], b1[14] .. b1[8]
output [7:0] b2; // b2[7], b2[6] .. b1[0]
input clk; // single signal
You can also define multi-bit busses.
  [ range_start : range_end ]
Example:

## Slide 94: Basic Syntax
// Single line comments start with a //
/* Multiline comments
are defined like this */
Verilog is case sensitive:
  SomeName and somename are not the same!
Names cannot start with numbers:
  2good is not a valid name
Whitespace is ignored

## Slide 95: Good Practices
Develop/use a consistent naming style
Use MSB to LSB ordering for busses (little-endian)
  Try using “a[31:0]” and not “a[0:31]”
Define one module per file
  Makes managing your design hierarchy easier
Use a file name that equals module name
  i.e. module TryThis is defined in a file called TryThis.v

## Slide 96: Structural HDL: Instantiating a Module

## Slide 97: What Happens with HDL code?
Automatic Synthesis (combine)
  Modern tools are able to map a behavioral HDL code into gate-level schematics
  They can perform many optimizations
  … however they can not guarantee that a solution is optimal
  Most common way of Digital Design these days
Simulation
  Allows the behavior of the circuit to be verified without actually manufacturing the circuit
  Simulators can work on behavioral or gate-level schematics

## Slide 98: Behavioral HDL: Defining Functionality
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
assign y = ~a & ~b & ~c |
a & ~b & ~c |
a & ~b & c;
endmodule

## Slide 99: Behavioral HDL: Synthesis Results

## Slide 100: Behavioral HDL: Simulating the Circuit

## Slide 101: Bitwise Operators
module gates(input [3:0] a, b,
output [3:0] y1, y2, y3, y4, y5);
/* Five different two-input logic
gates acting on 4 bit busses */
assign y1 = a & b; // AND
assign y2 = a | b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a | b); // NOR
endmodule

## Slide 102: Bitwise Operators: Synthesis Results

## Slide 103: Reduction Operators
module and8(input [7:0] a,
output y);
assign y = &a;
// &a is much easier to write than
// assign y = a[7] & a[6] & a[5] & a[4] &
// a[3] & a[2] & a[1] & a[0];
endmodule

## Slide 104: Reduction Operators: assign y = &a;

## Slide 105: Conditional Assignment
module mux2(input [3:0] d0, d1,
input s,
output [3:0] y);
assign y = s ? d1 : d0;
// if (s) then y=d1 else y=d0;
endmodule
? : is also called a ternary operator as it operates on three inputs:
  s
  d1
  d0.

## Slide 106: Conditional Assignment: y = s ? d1: d0;

## Slide 107: More Conditional Assignments
module mux4(input [3:0] d0, d1, d2, d3
input [1:0] s,
output [3:0] y);
assign y = s[1] ? ( s[0] ? d3 : d2)
: ( s[0] ? d1 : d0);
// if (s1) then
// if (s0) then y=d3 else y=d2
// else
// if (s0) then y=d1 else y=d0
endmodule

## Slide 108: Number Representation in Verilog
Verilog | Stored Number | Verilog | Stored Number
4’b1001 | 1001 | 4’d5 | 0101
8’b1001 | 0000 1001 | 12’hFA3 | 1111 1010 0011
8’b0000_1001 | 0000 1001 | 8’o12 | 00 001 010
8’bxX0X1zZ1 | XX0X 1ZZ1 | 4’h7 | 0111
‘b01 | 0000 .. 0001 | 12’h0 | 0000 0000 0000

## Slide 109: Precedence of operations in Verilog
~ | NOT
*, /, % | mult, div, mod
+, - | add,sub
<<, >> | shift
<<<, >>> | arithmetic shift
<, <=, >, >= | comparison
==, != | equal, not equal
&, ~& | AND, NAND
^, ~^ | XOR, XNOR
¦, ~¦ | OR, NOR
?: | ternary operator
Highest
Lowest

## Slide 110: What have seen so far:
Describing structural hierarchy with Verilog
  Instantiate modules in an other module
Writing simple logic equations
  We can write AND, OR, XOR etc
Multiplexer functionality
  If … then … else
We can describe constants
But there is more:

## Slide 111: Verilog tips
Do not write C-code
  Think hardware, not algorithms
    Verilog is inherently parallel
    Compilers don’t map algorithms to circuits well
Do describe hardware circuits
  First draw a dataflow diagram
  Then start coding

## Slide 112: The Verilog Language
Structural and behavioral model of Verilog language For reference Only

## Slide 113: The Verilog Language
Originally a modeling language for a very efficient event-driven digital logic simulator
Later pushed into use as a specification language for logic synthesis
Now, one of the two most commonly-used languages in digital hardware design (VHDL is the other)
Virtually every chip (FPGA, ASIC, etc.) is designed in part using one of these two languages
Combines structural and behavioral modeling styles

## Slide 114: Structural Modeling
When Verilog was first developed (1984) most logic simulators operated on netlists
Netlist: list of gates and how they’re connected
A natural representation of a digital logic circuit
Not the most convenient way to express test benches

## Slide 115: Behavioral Modeling
A much easier way to write testbenches
Also good for more abstract models of circuits
  Easier to write
  Simulates faster
More flexible
Provides sequencing
Verilog succeeded in part because it allowed both the model and the testbench to be described together

## Slide 116: How Verilog Is Used
Virtually every ASIC is designed using either Verilog or VHDL (a similar language)
Behavioral modeling with some structural elements
“Synthesis subset”
  Can be translated using Synopsys’ Design Compiler or others into a netlist
Design written in Verilog
Simulated to death to check functionality
Synthesized (netlist generated)
Static timing analysis to check timing

## Slide 117: Two Main Components of Verilog
Concurrent, event-triggered processes (behavioral)
  Initial and Always blocks
  Imperative code that can perform standard data manipulation tasks (assignment, if-then, case)
  Processes run until they delay for a period of time or wait for a triggering event
Structure (Plumbing)
  Verilog program build from modules with I/O interfaces
  Modules may contain instances of other modules
  Modules contain local signals, etc.
  Module configuration is static and all run concurrently

## Slide 118: Two Main Data Types
Nets represent connections between things
  Do not hold their value
  Take their value from a driver such as a gate or other module
  Cannot be assigned in an initial or always block
Regs represent data storage
  Behave exactly like memory in a computer
  Hold their value until explicitly assigned in an initial or always block
  Never connected to something
  Can be used to model latches, flip-flops, etc., but do not correspond exactly
  Shared variables with all their attendant problems

## Slide 119: Discrete-event Simulation
Basic idea: only do work when something changes
Centered around an event queue
  Contains events labeled with the simulated time at which they are to be executed
Basic simulation paradigm
  Execute every event for the current simulated time
  Doing this changes system state and may schedule events in the future
  When there are no events left at the current time instance, advance simulated time soonest event in the queue

## Slide 120: Four-valued Data
Verilog’s nets and registers hold four-valued data
0, 1
  Obvious
Z
  Output of an undriven tri-state driver
  Models case where nothing is setting a wire’s value
X
  Models when the simulator can’t decide the value
  Initial state of registers
  When a wire is being driven to 0 and 1 simultaneously
  Output of a gate with Z inputs

## Slide 121: Four-valued Logic
Logical operators work on three-valued logic
0 1 X Z
0 0 0 0 0
1 0 1 X X
X 0 X X X
Z 0 X X X
Output 0 if one input is 0
Output X if both inputs are gibberish

## Slide 122: Structural Modeling

## Slide 123: Nets and Registers
Wires and registers can be bits, vectors, and arrays
wire a; // Simple wire
tri [15:0] dbus; // 16-bit tristate bus
tri #(5,4,8) b; // Wire with delay
reg [-1:4] vec; // Six-bit register
trireg (small) q; // Wire stores a small charge
integer imem[0:1023]; // Array of 1024 integers
reg [31:0] dcache[0:63]; // A 32-bit memory

## Slide 124: Modules and Instances
Basic structure of a Verilog module:
module mymod(output1, output2, … input1, input2);
output output1;
output [3:0] output2;
input input1;
input [2:0] input2;
…
endmodule
Verilog convention lists outputs first

## Slide 125: Instantiating a Module
Instances of
module mymod(y, a, b);
look like
mymod mm1(y1, a1, b1); // Connect-by-position
mymod (y2, a1, b1),
(y3, a2, b2); // Instance names omitted
mymod mm2(.a(a2), .b(b2), .y(c2)); // Connect-by-name

## Slide 126: Gate-level Primitives
Verilog provides the following:
and nand logical AND/NAND
or nor logical OR/NOR
xor xnor logical XOR/XNOR
buf not buffer/inverter
bufif0 notif0 Tristate with low enable
bifif1 notif1 Tristate with high enable

## Slide 127: Delays on Primitive Instances
Instances of primitives may include delays
buf b1(a, b); // Zero delay
buf #3 b2(c, d); // Delay of 3
buf #(4,5) b3(e, f); // Rise=4, fall=5
buf #(3:4:5) b4(g, h); // Min-typ-max

## Slide 128: User-Defined Primitives
Way to define gates and sequential elements using a truth table
Often simulate faster than using expressions, collections of primitive gates, etc.
Gives more control over behavior with X inputs
Most often used for specifying custom gate libraries

## Slide 129: A Carry Primitive
primitive carry(out, a, b, c);
output out;
input a, b, c;
table
00? : 0;
0?0 : 0;
?00 : 0;
11? : 1;
1?1 : 1;
?11 : 1;
endtable
endprimitive
Always have exactly one output
Truth table may include don’t-care (?) entries

## Slide 130: A Sequential Primitive
Primitive dff( q, clk, data);
output q; reg q;
input clk, data;
table
// clk data q new-q
(01) 0 : ? : 0; // Latch a 0
(01) 1 : ? : 1; // Latch a 1
(0x) 1 : 1 : 1; // Hold when d and q both 1
(0x) 0 : 0 : 0; // Hold when d and q both 0
(?0) ? : ? : -; // Hold when clk falls
? (??) : ? : -; // Hold when clk stable
endtable
endprimitive

## Slide 131: Continuous Assignment
Another way to describe combinational function
Convenient for logical or datapath specifications
wire [8:0] sum;
wire [7:0] a, b;
wire carryin;
assign sum = a + b + carryin;
Define bus widths
Continuous assignment: permanently sets the value of sum to be a+b+carryin
Recomputed when a, b, or carryin changes

## Slide 132: Behavioral Modeling

## Slide 133: Initial and Always Blocks
Basic components for behavioral modeling
initial
begin
… imperative statements …
end
Runs when simulation starts
Terminates when control reaches the end
Good for providing stimulus
always
begin
… imperative statements …
end
Runs when simulation starts
Restarts when control reaches the end
Good for modeling/specifying hardware

## Slide 134: Initial and Always
Run until they encounter a delay
initial begin
#10 a = 1; b = 0;
#10 a = 0; b = 1;
end
or a wait for an event
always @(posedge clk) q = d;
always begin wait(i); a = 0; wait(~i); a = 1; end

## Slide 135: Procedural Assignment
Inside an initial or always block:
sum = a + b + cin;
Just like in C: RHS evaluated and assigned to LHS before next statement executes
RHS may contain wires and regs
  Two possible sources for data
LHS must be a reg
  Primitives or cont. assignment may set wire values

## Slide 136: Imperative Statements
if (select == 1) y = a;
else y = b;
case (op)
2’b00: y = a + b;
2’b01: y = a – b;
2’b10: y = a ^ b;
default: y = ‘hxxxx;
endcase

## Slide 137: For Loops
A increasing sequence of values on an output
reg [3:0] i, output;
for ( i = 0 ; i <= 15 ; i = i + 1 ) begin
output = i;
#10;
end

## Slide 138: While Loops
A increasing sequence of values on an output
reg [3:0] i, output;
i = 0;
while (I <= 15) begin
output = i;
#10 i = i + 1;
end

## Slide 139: Modeling A Flip-Flop With Always
Very basic: an edge-sensitive flip-flop
reg q;
always @(posedge clk)
q = d;
q = d assignment runs when clock rises: exactly the behavior you expect

## Slide 140: Blocking vs. Nonblocking
Verilog has two types of procedural assignment
Fundamental problem:
  In a synchronous system, all flip-flops sample simultaneously
  In Verilog, always @(posedge clk) blocks run in some undefined sequence

## Slide 141: A Flawed Shift Register
This doesn’t work as you’d expect:
reg d1, d2, d3, d4;
always @(posedge clk) d2 = d1;
always @(posedge clk) d3 = d2;
always @(posedge clk) d4 = d3;
These run in some order, but you don’t know which

## Slide 142: Non-blocking Assignments
This version does work:
reg d1, d2, d3, d4;
always @(posedge clk) d2 <= d1;
always @(posedge clk) d3 <= d2;
always @(posedge clk) d4 <= d3;
Nonblocking rule:
RHS evaluated when assignment runs
LHS updated only after all events for the current instant have run

## Slide 143: Nonblocking Can Behave Oddly
A sequence of nonblocking assignments don’t communicate
a = 1;
b = a;
c = b;
Blocking assignment:
a = b = c = 1
a <= 1;
b <= a;
c <= b;
Nonblocking assignment:
a = 1
b = old value of a
c = old value of b

## Slide 144: Nonblocking Looks Like Latches
RHS of nonblocking taken from latches
RHS of blocking taken from wires
a = 1;
b = a;
c = b;
a <= 1;
b <= a;
c <= b;
1
a
b
c
“
”
a
b
c
1
“
”

## Slide 145: Building Behavioral Models

## Slide 146: Modeling FSMs Behaviorally
There are many ways to do it:
Define the next-state logic combinationally and define the state-holding latches explicitly
Define the behavior in a single always @(posedge clk) block
Variations on these themes

## Slide 147: FSM with Combinational Logic
module FSM(o, a, b, reset);
output o;
reg o;
input a, b, reset;
reg [1:0] state, nextState;
always @(a or b or state)
case (state)
2’b00: begin
nextState = a ? 2’b00 : 2’b01;
o = a & b;
end
2’b01: begin nextState = 2’b10; o = 0; end
endcase
Combinational block must be sensitive to any change on any of its inputs
(Implies state-holding elements otherwise)
Output o is declared a reg because it is assigned procedurally, not because it holds state

## Slide 148: FSM with Combinational Logic
module FSM(o, a, b, reset);
…
always @(posedge clk or reset)
if (reset)
state <= 2’b00;
else
state <= nextState;
Latch implied by sensitivity to the clock or reset only

## Slide 149: FSM from Combinational Logic
always @(a or b or state)
case (state)
2’b00: begin
nextState = a ? 2’b00 : 2’b01;
o = a & b;
end
2’b01: begin nextState = 2’b10; o = 0; end
endcase
always @(posedge clk or reset)
if (reset)
state <= 2’b00;
else
state <= nextState;
This is a Mealy machine because the output is directly affected by any change on the input

## Slide 150: FSM from a Single Always Block
module FSM(o, a, b);
output o; reg o;
input a, b;
reg [1:0] state;
always @(posedge clk or reset)
if (reset) state <= 2’b00;
else case (state)
2’b00: begin
state <= a ? 2’b00 : 2’b01;
o <= a & b;
end
2’b01: begin state <= 2’b10; o <= 0; end
endcase
Expresses Moore machine behavior:
Outputs are latched
Inputs only sampled at clock edges
Nonblocking assignments used throughout to ensure coherency.
RHS refers to values calculated in previous clock cycle

## Slide 151: Simulating Verilog

## Slide 152: How Are Simulators Used?
Testbench generates stimulus and checks response
Coupled to model of the system
Pair is run simultaneously
Testbench
System Model
Stimulus
Response
Result checker

## Slide 153: Writing Testbenches
module test;
reg a, b, sel;
mux m(y, a, b, sel);
initial begin
$monitor($time,, “a = %b b=%b sel=%b y=%b”,
a, b, sel, y);
a = 0; b= 0; sel = 0;
#10 a = 1;
#10 sel = 1;
#10 b = 1;
end
Inputs to device under test
Device under test
$monitor is a built-in event driven “printf”
Stimulus generated by sequence of assignments and delays

## Slide 154: Simulation Behavior
Scheduled using an event queue
Non-preemptive, no priorities
A process must explicitly request a context switch
Events at a particular time unordered
Scheduler runs each event at the current time, possibly scheduling more as a result

## Slide 155: Two Types of Events
Evaluation events compute functions of inputs
Update events change outputs
Split necessary for delays, nonblocking assignments, etc.
Evaluation event reads values of b and c, adds them, and schedules an update event
a <= b + c
Update event writes new value of a and schedules any evaluation events that are sensitive to a change on a

## Slide 156: Simulation Behavior
Concurrent processes (initial, always) run until they stop at one of the following
#42
  Schedule process to resume 42 time units from now
wait(cf & of)
  Resume when expression “cf & of” becomes true
@(a or b or y)
  Resume when a, b, or y changes
@(posedge clk)
  Resume when clk changes from 0 to 1

## Slide 157: Simulation Behavior
Infinite loops are possible and the simulator does not check for them
This runs forever: no context switch allowed, so ready can never change
while (~ready)
count = count + 1;
Instead, use
wait(ready);

## Slide 158: Simulation Behavior
Race conditions abound in Verilog
These can execute in either order: final value of a undefined:
always @(posedge clk) a = 0;
always @(posedge clk) a = 1;

## Slide 159: Simulation Behavior
Semantics of the language closely tied to simulator implementation
Context switching behavior convenient for simulation, not always best way to model
Undefined execution order convenient for implementing event queue

## Slide 160: Verilog and Logic Synthesis

## Slide 161: Logic Synthesis
Verilog is used in two ways
  Model for discrete-event simulation
  Specification for a logic synthesis system
Logic synthesis converts a subset of the Verilog language into an efficient netlist
One of the major breakthroughs in designing logic chips in the last 20 years
Most chips are designed using at least some logic synthesis

## Slide 162: Logic Synthesis
Takes place in two stages:
Translation of Verilog (or VHDL) source to a netlist
  Register inference
Optimization of the resulting netlist to improve speed and area
  Most critical part of the process
  Algorithms very complicated and beyond the scope of this class: Take Prof. Nowick’s class for details

## Slide 163: Translating Verilog into Gates
Parts of the language easy to translate
  Structural descriptions with primitives
    Already a netlist
  Continuous assignment
    Expressions turn into little datapaths
Behavioral statements the bigger challenge

## Slide 164: What Can Be Translated
Structural definitions
  Everything
Behavioral blocks
  Depends on sensitivity list
  Only when they have reasonable interpretation as combinational logic, edge, or level-sensitive latches
  Blocks sensitive to both edges of the clock, changes on unrelated signals, changing sensitivity lists, etc. cannot be synthesized
User-defined primitives
  Primitives defined with truth tables
  Some sequential UDPs can’t be translated (not latches or flip-flops)

## Slide 165: What Isn’t Translated
Initial blocks
  Used to set up initial state or describe finite testbench stimuli
  Don’t have obvious hardware component
Delays
  May be in the Verilog source, but are simply ignored
A variety of other obscure language features
  In general, things heavily dependent on discrete-event simulation semantics
  Certain “disable” statements
  Pure events

## Slide 166: Register Inference
The main trick
reg does not always equal latch
Rule: Combinational if outputs always depend exclusively on sensitivity list
Sequential if outputs may also depend on previous values

## Slide 167: Register Inference
Combinational:
reg y;
always @(a or b or sel)
if (sel) y = a;
else y = b;
Sequential:
reg q;
always @(d or clk)
if (clk) q = d;
Sensitive to changes on all of the variables it reads
Y is always assigned
q only assigned when clk is 1

## Slide 168: Register Inference
A common mistake is not completely specifying a case statement
This implies a latch:
always @(a or b)
case ({a, b})
2’b00 : f = 0;
2’b01 : f = 1;
2’b10 : f = 1;
endcase
f is not assigned when {a,b} = 2b’11

## Slide 169: Register Inference
The solution is to always have a default case
always @(a or b)
case ({a, b})
2’b00: f = 0;
2’b01: f = 1;
2’b10: f = 1;
default: f = 0;
endcase
f is always assigned

## Slide 170: Inferring Latches with Reset
Latches and Flip-flops often have reset inputs
Can be synchronous or asynchronous
Asynchronous positive reset:
always @(posedge clk or posedge reset)
if (reset)
q <= 0;
else q <= d;

## Slide 171: Simulation-synthesis Mismatches
Many possible sources of conflict
Synthesis ignores delays (e.g., #10), but simulation behavior can be affected by them
Simulator models X explicitly, synthesis doesn’t
Behaviors resulting from shared-variable-like behavior of regs is not synthesized
  always @(posedge clk) a = 1;
  New value of a may be seen by other @(posedge clk) statements in simulation, never in synthesis

## Slide 172: Compared to VHDL
Verilog and VHDL are comparable languages
VHDL has a slightly wider scope
  System-level modeling
  Exposes even more discrete-event machinery
VHDL is better-behaved
  Fewer sources of nondeterminism (e.g., no shared variables)
VHDL is harder to simulate quickly
VHDL has fewer built-in facilities for hardware modeling
VHDL is a much more verbose language
  Most examples don’t fit on slides